## Slide 1: What is the Control Logic ?
Part of the computer that is outputting the Control Signals based on each specific instruction.
So far we have been using our Arduino Mega Shield to set the control signals to High/Low
We are building the control logic to output the required Control signals for each specific instruction.

## Slide 2: How a computer execute programs ?
Program Counter
When the computer starts, Program counter starts counting from 0
With each step, the value is put on the BUS
Signal : CO
Memory Address Register
MAR reads the value from the BUS and set the Address to the value
Signal : MI
Memory (FLASH/RAM)
Outputs the content of memory address on the BUS
Signal : RO
Micro Step Counter
A counter that counts micro steps
Flag Register
The Status of Flags saved into this register
Signal : FI
Control Logic
Instruction register
BUS content is the next instruction to be executed
Signal : II
Next Step
Signal : CE
Control ROM
Output is Addressing a ROM
CE ME CI CO AI AO BI BO MI RO FI EO .…..

## Slide 3: Control Logic in Bravo
2 x SST39SF010
Each 128 KB
Micro Step Counter
A counter that counts micro steps (4 Bits)
Flag Register
The Status of Flags saved into this register (3 Bits)
Signal : EOFI
Control Logic
Instruction register
BUS content is the next instruction to be executed (6 Bits)
Signal : HI + CEME = II
CE ME CI CO AI AO BI BO MI RO FI EO .…..
LSB
MSB
8 Signals
8 Signals
Control ROMs

## Slide 4: How Bravo execute programs ?
CO , MI
CO, MI, HI
RO, HI, CEME
Fetch Instruction
CO , MI
CO, MI, HI
RO, HI, CEME
RO, AI, CEME,IC
Example: LDI

## Slide 5: What is a program ?
Program
to add
X & Y
LDI 10
Instructions
1
2
3
Load X value directly into A register
Load Y value from memory and ADD it
Output the result
ADD 01 80
OUT
Operand
(Memory Location, Contains Y)
Instruction
(Mnemonics used in programming)
LDI 10
Load value of 10 directly to A register
Load the Value of memory Address 8001(HEX) into B register
Output the content of the BUS
Signals
CO , MI
CO, MI, HI
RO, HI, CEME
RO, AI, CEME,IC
Micro steps
Operand
(Value of X)
Instruction

## Slide 6: Microcode in Bravo
Flags (3 bits)
8 possible combinations
Instruction(6 bits)
64 different instructions
Micro Steps(4 bits)
16 Micro steps
+
+
4 + 13 bits
Each Instruction is assigned a binary value, For Example
LDI is assigned value of 14
STA is assigned value 21
Etc..
0000 (4 bits)
Mnemonic | Filler Bits (4 Bits) | Flags (3 Bits) | Instruction (6 Bits) | Steps (4Bits) |  | Control Signal
LDI | 0000 | 000 | 001110 | 0000 | Step0 | CO, MI
LDI | 0000 | 000 | 001110 | 0001 | Step1 | CO,MI,HI
LDI | 0000 | 000 | 001110 | 0010 | Step2 | RO,HI,CEME
LDI | 0000 | 000 | 001110 | 0011 | Step3 | RO,AI,CEME,IC
LDI | 0000 | 000 | 001110 | 0100 | Step4 | -
LDI | 0000 | 000 | 001110 | 0101 | …. | -
Total of 17 bits , addressing ROMs using 17 address lines

## Slide 7: Microcode in Bravo
Flags (3 bits)
8 possible combinations
Instruction(6 bits)
64 different instructions
Micro Steps(4 bits)
16 Micro steps
x
x
8192 Total Micro Instructions , 8K
LDA 101001 Step0 0000 CO|MI
LDA 101001 Step1 0001 CO|MI|HI
LDA 101001 Step2 0010 RO|HI|CEME
LDA 101001 Step3 0011 RO|BI|CEME
. . . .
. . . .
LDA 101001 Step15 1111 .
LDA 101001 Step0 0000 CO|MI
LDA 101001 Step1 0001 CO|MI|HI
LDA 101001 Step2 0010 RO|HI|CEME
LDA 101001 Step3 0011 RO|BI|CEME
. . . .
. . . .
LDA 101001 Step15 1111 .
LDA 101001 Step0 0000 CO|MI
LDA 101001 Step1 0001 CO|MI|HI
LDA 101001 Step2 0010 RO|HI|CEME
LDA 101001 Step3 0011 RO|BI|CEME
. . . .
. . . .
LDA 101001 Step15 1111 .
3 Flags
(8 combinations)
000
001
010
.